## Slide 1: Methods of Research
Paper presentation
Ivan John Naparota | October 19, 2018

## Slide 2: Optimizing the configuration of a façade module for office buildings by means of integrated thermal and lighting simulations in a total energy perspective
Francesco Goia, Matthias Haase, Marco Perino
Goia, F., Haase, M., & Perino, M. (2013). Optimizing the configuration of a façade module for office buildings by means of integrated thermal and lighting simulations in a total energy perspective. Applied Energy, 108, 515–527. https://doi.org/10.1016/j.apenergy.2013.02.063

## Slide 3: Background
Finding the optimum façade configuration in low energy buildings (energy efficient buildings):
Mostly through analysis of cooling and/or heating energy demand only
Mostly neglecting its implication on the artificial lighting energy demand and visual environment
When dynamic solar shading is considered, there is complexity in thermal-lighting simulations

## Slide 4: Goal
Present a methodology in finding the optimum façade configuration (window-wall ratio) through analyses of total energy demand (lighting, cooling, and heating) and visual environment in a low energy office building with dynamic solar shading.

## Slide 5: Specific Objectives
To identify the optimum value of solar shading that will give the least total energy consumption
  Simulate different activation set point of the solar shading device for every WWR value and orientation
  Process output data from simulation and arrive to the optimum set point value for each WWR value and orientation; analyse the effect of different set points to ETOT
To identify the optimum value of window-wall ratio for every orientation that will give the least total energy consumption
  Simulate different WWR values for every orientation applying the optimum set-points
  Process output data from simulation and arrive to the optimum WWR value for every orientation
  Analyse the behaviour of front façade with respect to the back façade
  Compare worst and optimum WWR value with respect to ETOT
To analyse the implication of WWR values on the visual environment
  Daylight Autonomy metric
  Useful Day-light Illuminance metric
To test the robustness of the WWR value using sensitivity analysis
  Sensitivity analysis of the optimum WWR value with varying surface area-to-volume ratio
  Sensitivity analysis of the optimum WWR value with varying SCOP for heating and cooling

## Slide 6: Experimental Flow Diagram
4 set-points
5 WWR
4 orientations
Simulation
EH
EC
EL
Data process
Optimum
Set point
values
Simulation
2 coupled orientations
5 WWR front
5 WWR back
EH
EC
EL
UDI
DA
Data process
Optimum WWR
Optimum WWR
Different SA:V
Different SCOP for heating/cooling
Analyse/Compare
Robustness

## Slide 7: Experimental Design
To identify the optimum value of solar shading
  Simulate different activation set point of the solar shading device for every WWR value and orientation
4 set-points
5 WWR
4 orientations
Baseline Model
EH
EC
EL

## Slide 8: Experimental Design
To identify the optimum value of window-wall ratio for every orientation
  Simulate different WWR values for every orientation applying the optimum set-points
To test the robustness of the WWR value
  Sensitivity analysis of the optimum WWR value with varying surface area-to-volume ratio
  Sensitivity analysis of the optimum WWR value with varying SCOP for heating and cooling
Optimum
Set point
values
B2: SA/V=.25
B1: SA/V=.20
B3: SA/V=.30
HVACeff = 2.6, 3.8
HVACeff = 2.6, 4.75 | 2.6, 2.85 | 3.25, 3.8 |1.95, 3.8
2 coupled orientations
5 WWR front
5 WWR back
EH
EC
EL
EH
EC
EL
EH
EC
EL

## Slide 9: Experimental Design
To analyse the implication of WWR values to visual environment
  Daylight Autonomy metric [32]
  Useful Day-light Illuminance metric [33]
Optimum
Set point
values
B2: SA/V=.25
HVACeff = 2.6, 3.8
2 coupled orientations
5 WWR front
5 WWR back
Useful Daylight Illuminance
Daylight Autonomy

## Slide 10: Information Flow Diagram
To identify the optimum value of solar shading
  Process output data from simulation and arrive to the optimum set point value for each WWR value and orientation; analyse the effect of different set points to ETOT
EH
EC
EL
Optimum Set point values
Extra Energy Demand as a function of different activation set-points

## Slide 11: Information Flow Diagram
To identify the optimum value of window-wall ratio for every orientation
  Simulate different WWR values for every orientation applying the optimum set-points
  Process output data from simulation and arrive to the optimum WWR value for every orientation
  Analyse the behaviour of front façade with respect to the back façade
  Compare worst and optimum WWR value with respect to ETOT
EH
EC
EL
Optimum WWR
EH
EC
EL
EH
EC
EL
Optimum WWR
Optimum WWR
ETOT

## Slide 12: Results and Discussions
To identify the optimum value of solar shading and analyse its implications
  Simulate different activation set point of the solar shading device for every WWR value and orientation
  Process output data from simulation and arrive to the optimum set point value for each WWR value and orientation; analyse the effect of different set points to ETOT
Results:
Optimal set-point decreases as WWR value increases
No need for solar shading in the north façade

## Slide 13: Results and Discussions
To identify the optimum value of solar shading and analyse its implications
  Simulate different activation set point of the solar shading device for every WWR value and orientation
  Process output data from simulation and arrive to the optimum set point value for each WWR value and orientation; analyse the effect of different set points to ETOT
Results:
South – 6% least to optimum difference
West – 3-4% least to optimum difference
East – 4-6% least to optimum difference

## Slide 14: Results and Discussions
To identify the optimum value of window-wall ratio for every orientation
  Simulate different WWR values for every orientation applying the optimum set-points
  Process output data from simulation and arrive to the optimum WWR value for every orientation
  Analyse the behaviour of front façade with respect to the back façade
  Compare worst and optimum WWR value with respect to Etot
Results
Optimum WWR value is between 35-45%
Back facade WWR value has no significant effect on the performance
of front façade
South – optimal to worst = 6% difference | North – optimal to worst = 11% difference
West – optimal to worst = 7% difference | East – optimal to worst = 8-9% difference

## Slide 15: Results and Discussions
To analyse the implication of WWR values to the visual environment
  Daylight Autonomy metric
  Useful Day-light Illuminance metric
Results:
DA > 50% is obtained for façade configurations with WWR > 30% for every orientation
In the range where the optimal façade configurations lie (i.e. 35% < WWR < 50%), the UDI>2000 is about 20% for a south exposed façade, and about 12% in east/west exposed façades

## Slide 16: Results and Discussions
To test the robustness of the WWR value
  Sensitivity analysis of the optimum WWR value with varying surface area-to-volume ratio
  Sensitivity analysis of the optimum WWR value with varying SCOP for heating and cooling
Results:
The analysis points out that the building geometry affects the total energy demand. However, it also shows that the optimal WWR is independent from the building geometry.

## Slide 17: Results and Discussions
To test the robustness of the WWR value
  Sensitivity analysis of the optimum WWR value with varying surface area-to-volume ratio
  Sensitivity analysis of the optimum WWR value with varying SCOP for heating and cooling
Results:
The optimal WWR values are independent from the efficiency of the heating systems.
Higher efficiency of cooling tolerates a higher WWR value

## Slide 18: Conclusion
WWR value has a low influence to the total energy consumption (Lighting, Cooling, Heating) of advanced façade module.
The minimum total primary energy demand is always achieved when WWR is in the range of 35–45%; and with satisfying day-lighting performance
The analyses show little dependence of Etot(WWR) on the building geometry and the HVAC efficiency
Set-point for solar shading will cause up to 11% more energy demand if not properly configured